## Slide 1: CHAPTER 4 Optimal Predictive Control 4 Analysis of the performance index
Anthony Rossiter

## Slide 2: Background: Optimal MPC (OMPC)
Take the daul-mode predictions based around the implementation of an LQR regulator and some perturbations.
Optimise predicted performance w.r.t. to the perturbations in the transient mode and implement the first value.
Transient mode
Terminal mode

## Slide 3: Background continued
The previous video derived the algebra for computing the performance index J assuming the predictions are based on perturbations about an unconstrained closed-loop optimal.
In summary the nominal performance index J becomes:
The matrices are defined from:

## Slide 4: Aims
This video investigates the new form of the performance index in detail in order to understand the role and structure of each of the matrices Sx, Sxc, Sc.
This insight will prove useful.
We will begin with a few numeric examples to set the scene.

## Slide 5: Example 1
Take some examples and investigate the matrices Sx, Sxc, Sc for different choices of nc.
Also consider the impact of changing Q and R.
video_4_4_example1
video_4_4_example2

## Slide 6: Observations
The value of Sx does not change with the control horizon nc.
The values in Sc do not change with the control horizon nc – in essence Sc is a diagonal matrix with the same values in the diagonal.
Sxc is always zero.
When Q,R are changed, although the underlying values change, the same pattern is observed.

## Slide 7: Example 2
Take a MIMO example and investigate the matrices Sx, Sxc, Sc for different choices of nc.
Also consider the impact of changing Q and R.
video_4_4_example3
Same conclusions! The value of Sx does not change with the control horizon nc. The values in Sc do not change with the control horizon nc. Sxc is always zero

## Slide 8: Understanding the observations 1
Are these observations intuitively obvious and if so, can they be proved?
Irrespective of the horizon nc, one can always choose the future values ck=0. In this case the cost is fixed.
Consequently it is obvious that the value of Sx cannot depend upon nc.
One might note however that the Sx term has no impact on the optimisation as this does not depend upon the d.o.f.

## Slide 9: Understanding the observations 2
Are these observations intuitively obvious and if so, can they be proved?
Recall, that by definition the optimal behaviour is given from u=-Kx and therefore, by definition, the optimal ck term must be zero.
The performance index is a quadratic in terms of the perturbation terms, but the optimal is known to be at the origin. Hence, rearranging J it is clear that:

## Slide 10: Understanding the observations 2
One can easily determine the relationship needed to show Sxc=0 as follows.

## Slide 11: Understanding the observations 3
The final parameter is Sc which appears to have a block diagonal structure.
This implies that:
Every perturbation term ck+i has an identical impact on the cost and there are no cross terms involving ck+i and ck+j

## Slide 12: Rationale for observation 3
This follows immediately from u=-Kx being the unconstrained optimal.
This means, irrespective of the predicted value of ck chosen at sample k, the optimal value of ck+1 will still be zero and have no dependence on ck; consequently no cross terms (off diagonals in Sc).
Given we deploy infinite horizons, the impact on the cost of ck and ck+1 must be identical; consequently all diagonal terms must be the same.
The observation that Sc is block diagonal with identical diagonal elements is exactly what we expected from video 2.

## Slide 13: Feedback control law
For completeness, it is worth doing the optimisation of J to determine the optimum value of the perturbation terms ck.
Consequently:
However, of course Sxc=0, so:
The optimal unconstrained control law
u=-Kx+c
is independent of the control horizon nc.

## Slide 14: Summary
Used argument and numerical example to investigate the structure of an OMPC performance index.
Shown that Sx is independent of the horizon (although of course also does not effect any optimisation).
Sxc must be zero (assumes predictions and cost both based around the LQR optimal).
Sc must be block diagonal with each block the same.
Reminded that although this means the optimal c=0 (we appear to have done nothing), this is setting up important ground work for constraint handling which is to come later.

## Slide 15
© 2014 University of Sheffield
This work is licensed under the Creative Commons Attribution 2.0 UK: England & Wales Licence. To view a copy of this licence, visit http://creativecommons.org/licenses/by/2.0/uk/ or send a letter to: Creative Commons, 171 Second Street, Suite 300, San Francisco, California 94105, USA.
It should be noted that some of the materials contained within this resource are subject to third party rights and any copyright notices must remain with these materials in the event of reuse or repurposing.
If there are third party images within the resource please do not remove or alter any of the copyright notices or website details shown below the image.
(Please list details of the third party rights contained within this work.
If you include your institutions logo on the cover please include reference to the fact that it is a trade mark and all copyright in that image is reserved.)
Anthony Rossiter
Department of Automatic Control and Systems Engineering
University of Sheffield
www.shef.ac.uk/acse