## Slide 1: CHAPTER 4 Optimal Predictive Control 8 MATLAB code and numerical examples
Anthony Rossiter

## Slide 2: Introduction
This chapter has developed both the OMPC and SOMPC algorithms, for the state space case, assuming no uncertainty, no constraints and a regulation scenario.
Next it is important to develop some implementation code to illustrate and test whether this approach is indeed simple and effective to apply.
It would also be interesting to explore the cost function and demonstrate this is indeed a Lyapunov function.
For SOMPC, we should investigate how the control law varies with nc.

## Slide 3: Sub-optimal dual mode MPC (SOMPC)
Take the dual-mode predictions based around the implementation of an arbitrary stabilising regulator and some perturbations.
Optimise predicted performance w.r.t. to the perturbations and implement the first value.
If u=-Kx is the LQR regulator for J, then we call this OMPC not SOMPC.

## Slide 4: Optimisation
The performance index can be simplified to:
Details of the matrices are covered in earlier videos.
Consequently, in the unconstrained case, the optimal control law is given as:
We will demonstrate code to compute and display J, c, u, y at every sample.
Also dependence of KSOMPC on nc.

## Slide 5: video4_8_example 1.m
OMPC simulation, SISO system, Vary nc
OBSERVATIONS
Cost is clearly monotonic (as expected if Lyapunov).
Responses are convergent (stabilised loop).
Perturbations are ZERO!
KSOMPC does not change with nc.

## Slide 6: video4_8_example2.m
SOMPC simulation, SISO system, vary nc
OBSERVATIONS
Cost is clearly monotonic (as expected if Lyapunov).
Responses are convergent (stabilised loop).
Perturbations are not zero and can be very large changes in optimised ck from one sample to the next (note some predicted values are ZERO!].
KSOMPC quite close to KOMPC even for nc=1.

## Slide 7: video4_8_example3.m
SOMPC simulation, MIMO system, vary nc
OBSERVATIONS
Cost is clearly monotonic (as expected if Lyapunov).
Responses are convergent (stabilised loop).
Perturbations are not zero and can be substantive change in n-step ahead predictions and what is actually implemented (due to assumption that c(k+nc)=0 in predictions).
KSOMPC quite close to KOMPC and gets closer as nc increases.
SOMPC has same weakness as GPC – mismatch between predictions and implementation.

## Slide 8: Conclusions
As expected both OMPC/SOMPC are stabilising and the numerical examples have monotonic cost functions.
As expected, the optimised perturbations for OMPC are ZERO.
SOMPC gives non-zero perturbations and although possibly an improvement on GPC (as has guaranteed stability through infinite horizons), one can argue similar conceptual weaknesses due to a mismatch between predictions and implementation with low nc.
SOMPC feedback tends towards OMPC for large nc.
Possible reasons for preferring SOMPC come later.

## Slide 9
© 2014 University of Sheffield
This work is licensed under the Creative Commons Attribution 2.0 UK: England & Wales Licence. To view a copy of this licence, visit http://creativecommons.org/licenses/by/2.0/uk/ or send a letter to: Creative Commons, 171 Second Street, Suite 300, San Francisco, California 94105, USA.
It should be noted that some of the materials contained within this resource are subject to third party rights and any copyright notices must remain with these materials in the event of reuse or repurposing.
If there are third party images within the resource please do not remove or alter any of the copyright notices or website details shown below the image.
(Please list details of the third party rights contained within this work.
If you include your institutions logo on the cover please include reference to the fact that it is a trade mark and all copyright in that image is reserved.)
Anthony Rossiter
Department of Automatic Control and Systems Engineering
University of Sheffield
www.shef.ac.uk/acse