## Slide 1: CHAPTER 4 Optimal Predictive Control 9 Tracking and disturbance rejection
Anthony Rossiter

## Slide 2: Introduction to dual-mode MPC
The previous videos in this chapter have presented a SOMPC control law for the regulation problem, assuming no uncertainty or constraints.
In practice there will be both uncertainty and non-zero targets, so this video considers what modifications are required to deal with that scenario.
The basic approach is to make use of the ‘unbiased’ prediction and costs developed in chapter 1.

## Slide 3: Unbiased performance indices
The key attribute of the performance index is that it is unbiased. Unbiased means that if we deploy the performance index at the correct steady-state, then it will propose that the input remains unchanged.
Most obvious terms to use in J are those which are zero at the correct steady-state.
Some common components, and hence a generic choice of J, that satisfy this requirement are listed here.
Disturbance model

## Slide 4: Unbiased steady-state estimates
The expected steady-state, perhaps sometime in the future obeys the following:
A disturbance estimate is required.
Typically, yss=r
Disturbance estimate updated every sample.

## Slide 5: Summary: Unbiased cost and control
Combining the observations of the previous 2 slides, a potential unbiased cost function would be:
A simple state feedback control law which ensures robust convergence to the correct steady-state is based on suitable deviation variables and thus:

## Slide 6: Sub-optimal dual mode MPC (SOMPC)
Take the dual-mode predictions based around the implementation of an arbitrary regulator using deviations variables and perturbations ck.
Optimise predicted performance w.r.t. to the perturbations and implement the first value.

## Slide 7: Simplifying the algebra
Assume the future disturbance and target are constant and define the deviation variables as follows:
Rewrite the model dynamics in terms of deviation variables.

## Slide 8: Simplifying the algebra
Rewrite the performance index and predicted control trajectory in terms of the deviation variables:
Apart from the simple variable change, this is identical in format to the SOMPC for regulation.

## Slide 9: Interim summary
SOMPC based on deviation variables will share the same properties as SOMPC for the regulation case.
Cost function will be Lyapunov (when the target and disturbance are constant).
Closed-loop guaranteed stabilising.
Deviation variables will tend to zero, which also implies offset free tracking.
It is implicit in practice that the disturbance estimate and hence values for xss,uss are updated every sample.
For now, assume disturbance is known.

## Slide 10: video4_9_example 1.m
OMPC simulation, SISO system, introduce a target change and a disturbance change.
Assume disturbance measureable for simplicity of code. [SYSTEM IS NON-MINIMUM PHASE!]
OBSERVATIONS
Cost is clearly monotonic while target and disturbance are constant.
Responses are convergent (stabilised loop).
Perturbations are ZERO!
Offset free tracking is obtained.

## Slide 11: video4_9_example2.m
SOMPC simulation, SISO system, introduce a target change and a disturbance change
OBSERVATIONS
Cost is clearly monotonic while target and disturbance are constant.
Responses are convergent (stabilised loop).
Perturbations are non-ZERO (as discussed in previous video)!
Offset free tracking is obtained.

## Slide 12: video4_9_example3.m
SOMPC/OMPC simulation, MIMO system.
OBSERVATIONS
Cost is clearly monotonic (as expected if Lyapunov).
Responses are convergent (stabilised loop).
Perturbations are not zero for SOMPC.
Offset free tracking and disturbance rejection is obtained.

## Slide 13: Conclusions
Extensions for OMPC/SOMPC for tracking and disturbance rejection are straightforward using the concepts from chapter 1. Ensure the performance index and the predictions are unbiased.
The proposal here defines the algorithms with respect to deviation variables (deviations about the expected steady-state). Examples show this works well.
Steady-state estimates must be updated every sample.

## Slide 14
© 2014 University of Sheffield
This work is licensed under the Creative Commons Attribution 2.0 UK: England & Wales Licence. To view a copy of this licence, visit http://creativecommons.org/licenses/by/2.0/uk/ or send a letter to: Creative Commons, 171 Second Street, Suite 300, San Francisco, California 94105, USA.
It should be noted that some of the materials contained within this resource are subject to third party rights and any copyright notices must remain with these materials in the event of reuse or repurposing.
If there are third party images within the resource please do not remove or alter any of the copyright notices or website details shown below the image.
(Please list details of the third party rights contained within this work.
If you include your institutions logo on the cover please include reference to the fact that it is a trade mark and all copyright in that image is reserved.)
Anthony Rossiter
Department of Automatic Control and Systems Engineering
University of Sheffield
www.shef.ac.uk/acse