## Slide 1: CHAPTER 6 Predictive Control with tracking 4 feedforward by trial and error in GPC
Anthony Rossiter

## Slide 2: Background
This chapter has established that the best choice of feedforward Pr in the GPC control law should utilise only some of the advance knowledge available.
This chapter shows how trial and error is an effective and simple mechanism for identifying suitable values for advance knowledge.
This video assumes stepwise target changes only.

## Slide 3: Feedforward definition with reduced a advance knowledge
Common terms can be combined as follows:
Now the feedforward term has just na coefficients.
BUT, how do we select an appropriate value for na?

## Slide 4: Poorly posed optimisations
The reason the default feedforward is poorly defined is because the optimisation is poorly defined.
As discussed earlier, it is rather obvious that one cannot track effectively a target change at the nth sample using control moves near the mth sample where n, m are not close together.
For a well defined optimisation, the flexibility in the predicted control trajectory must be sufficient to closely match the desired closed-loop trajectory.
These observations lead us to a systematic mechanism for creating a set of requirements.

## Slide 5: Thought experiment – ideal response
Consider a system with known open-loop dynamics and sketch an ideal input/output closed-loop step response (LQR would be a reasonable estimate).
TARGET
Determine the number and locations of samples over which the input and output trajectories undertake significant change.
na is the number of samples before that the input begins to move.
nu is the number of samples over which the principle input changes occur.

## Slide 6: Argument
If an ideal response only requires the input to move m samples before any target change, then na=m is sufficient to capture a prediction close to the ideal response.
If an ideal response requires m control moves, then nu=m is sufficient to capture the ideal input prediction.
It should be noted however, that the required numbers are dependent on the ‘ideal’ response which will thus vary with constraints and desired input activity.
This discussion excludes continuously varying targets although in practice the requirements for a step target usually suffice.

## Slide 7: Thought experiment 2
Chapter 3 gave some pragmatic approaches for selecting the input and output horizons.
The maximum useful value for na will be the maximal useful input horizon, as it is not productive for the input to move in advance of this.
In some cases na may be less than the advised value for nu.
These arguments are presented without any attempt to prove them rigorously as it is more important, in practice, to understand the limitations of a given implementation and to ensure that one is not guilty of asking for nonsense.

## Slide 8: Examples of using advance knowledge
The remainder of this video will give a number of examples to demonstrate how behaviour can be compared with various values of advance knowledge na.
The comparisons assume a fixed shape for the target. The author’s experience is that it is unlikely that a different na will be needed for different shapes of target.

## Slide 9: REMARK
These examples include the use of low nu for completeness.
However, given the insights of chapter 3, one could argue that in practice the results are most meaningful if and only if nu is large enough.

## Slide 10: video6_4_example1.m
The best value of na, with nu=2, seems to be around 2-3.
Runtime costs show that in fact na=2 is best for this case.

## Slide 11: video6_4_example1.m
Changing the weighting makes a big difference. Now the best value of na, with nu=2, seems to be around 5-7.
Runtime costs show that in fact na=5 is best for this case.

## Slide 12: video6_4_example1.m
The best value of na, with nu=4, seems to be around 3-4.
Runtime costs show that in fact na=5 is best for this case.
It would be pragmatic to choose na to be at the lower end of the ‘best’ values to avoid unnecessarily early anticipation.

## Slide 13: video6_4_example2.m
The best value of na, with nu=2, seems to be around 4-5.
Runtime costs show that in fact na=4 is best for this case.
Notice how in this case the best na is greater than nu.

## Slide 14: video6_4_example2.m
The best value of na, with nu=2 and a larger weight is notable larger than nu.
Runtime costs show that in fact na=8 is best for this case.
Notice how in this case the best na is much greater than nu.
[In fact, chapter 3 shows a higher nu should also be used!]

## Slide 15: video6_4_example2.m
The best value of na, with nu=5, seems to be around 5-6.
Runtime costs show that in fact any na>5 give similar answers for this case.

## Slide 16: video6_4_example3.m
The best value of na, with nu=2, seems to be around 2-3.
Runtime costs show that in fact na=2 is best with clear degradation as na increases.
Unlike in examples 1 and 2, here it is not advantageous for na>nu when nu is small.

## Slide 17: video6_4_example3.m
The best value of na, with nu=5, seems to be around 3-4.
Runtime costs show that in fact na=5 is best for this case.
A choice of na =3 or 4 would likely be good enough in this case, that is less than nu.

## Slide 18: video6_4_example4.m
The best value of na, with nu=2, seems to be around 2-3.
Runtime costs show that in fact any na=3 is best for this case.

## Slide 19: video6_4_example4.m
The best value of na, with nu=2, but larger weighting is increased. .
Runtime costs show that in fact any na=4 is best for this case.
For even larger weighting, larger values of na become preferable (as would larger values of nu in practice).

## Slide 20: video6_4_example4.m
The best value of na, with nu=5, seems to be around 2-4.
Runtime costs show that in fact na=5 is best for this case.
It would be pragmatic to choose na to be at the lower end of the ‘best’ values to avoid unnecessarily early anticipation.

## Slide 21: Summary
Demonstrated that it is straightforward to use a trial and error approach to explore the impact of changes in advance knowledge.
Common sense, backed up by simulations, illustrate the best choice of advance knowledge is in the same region as the choice of control horizon.
The best choice of advance knowledge (for step targets) is usually slightly greater than nu if nu is small, but may not be so if nu is large.
Best varies with the system and also the choice of input weighting.
One might equally guess that ‘best’ will vary enormously when constraints become active.

## Slide 22
© 2014 University of Sheffield
This work is licensed under the Creative Commons Attribution 2.0 UK: England & Wales Licence. To view a copy of this licence, visit http://creativecommons.org/licenses/by/2.0/uk/ or send a letter to: Creative Commons, 171 Second Street, Suite 300, San Francisco, California 94105, USA.
It should be noted that some of the materials contained within this resource are subject to third party rights and any copyright notices must remain with these materials in the event of reuse or repurposing.
If there are third party images within the resource please do not remove or alter any of the copyright notices or website details shown below the image.
(Please list details of the third party rights contained within this work.
If you include your institutions logo on the cover please include reference to the fact that it is a trade mark and all copyright in that image is reserved.)
Anthony Rossiter
Department of Automatic Control and Systems Engineering
University of Sheffield
www.shef.ac.uk/acse