## Slide 1: CHAPTER 6 Predictive Control with tracking 6 feed forward in dual-mode control
Anthony Rossiter

## Slide 2: Background
So far this chapter has demonstrated that the default GPC (same concept for most MPC) choice of feed forward may be quite poor.
However, changing the amount of advance knowledge available is a pragmatic and simple way of determining an effective feed forward for MPC.
This video begins a discussion of whether similar insights and solutions are applicable to dual-mode (infinite horizon) MPC algorithms.

## Slide 3: REMARK
The literature on dual-mode MPC has largely ignored the issue of feed forward and the default assumption is to use no advance knowledge.
An investigation of the algebra deployed in a typical dual mode strategy will indicate that it is messy to include variable values of na.
Moreover, a key assumption in typical dual-mode derivations is that the target is fixed and all the algebra, definitions of performance index, assumptions of global optimality and the like hinge on this.

## Slide 4: Dual mode paradigm
Terminal region in which
the control law u-uss=-K(x-xss)
satisfies constraints.
Initial state
trajectory
nc moves maximum
Terminal
State
In at most nc samples, predicted
state moves into the terminal
region while satisfying constraints.
Target is assumed fixed!

## Slide 5: Tracking in dual mode MPC (SOMPC)
Take the dual-mode predictions based around the implementation of an arbitrary regulator using deviations variables and perturbations ck.
Optimise predicted performance w.r.t. to the perturbations and implement the first value.
Note it is implicit that xss, uss are fixed throughout the prediction, and certainly beyond nc steps.

## Slide 6: Tracking in dual mode MPC (SOMPC)
It is implicit that xss, uss are fixed throughout the prediction. While one can modify J, typically the literature has not concerned itself with such details.
The next video goes through one possible algebraic mechanism for allowing time varying future target information.
WARNING: OMPC is premised on a constant state feedback being optimal (unconstrained case); this is not true for cases where the target is time varying!

## Slide 7: Summary
Introduced a key flaw in a typical OMPC set up and indicated that the typical literature may not easily allow for future target information.
The typical assumptions on ‘optimal’ terminal feedback and terminal costs are only valid where the target is constant.
The algebra for determining the performance index J needs some minor changes to allow for time varying future targets. These are given in the next video.

## Slide 8
© 2014 University of Sheffield
This work is licensed under the Creative Commons Attribution 2.0 UK: England & Wales Licence. To view a copy of this licence, visit http://creativecommons.org/licenses/by/2.0/uk/ or send a letter to: Creative Commons, 171 Second Street, Suite 300, San Francisco, California 94105, USA.
It should be noted that some of the materials contained within this resource are subject to third party rights and any copyright notices must remain with these materials in the event of reuse or repurposing.
If there are third party images within the resource please do not remove or alter any of the copyright notices or website details shown below the image.
(Please list details of the third party rights contained within this work.
If you include your institutions logo on the cover please include reference to the fact that it is a trade mark and all copyright in that image is reserved.)
Anthony Rossiter
Department of Automatic Control and Systems Engineering
University of Sheffield
www.shef.ac.uk/acse