## Slide 1: Predictive control 10 ensuring unbiased prediction
Anthony Rossiter

## Slide 2: Introduction
The previous videos have shown how one can form compact forms for predictions using state space, CARIMA and step response models.
However, little attention was given to the accuracy of these predictions in the presence of disturbances and parameter uncertainty.
It transpires that the most important time to be accurate is in the steady-state. If I am in the right place I do not want the prediction model suggesting that I will move from that place when that is untrue!
This video considers how one can ensure that the predictions are unbiased in the steady-state.

## Slide 3: Background on uncertainty
A simple disturbance model will be used in this section, hence assume the system can be represented as:
Also, in practice only estimates of the parameters of G are known.

## Slide 4: Background
Consider the steady-state scenario given here.
Which predictions do you expect, assuming the disturbance and input do not change?
past
future
If the future output predictions do not match the steady-state, they predictions are said to be biased.

## Slide 5: Requirements
There is a need to check the prediction equations from the earlier videos and establish whether these are biased or not.
These tests must allow for parameter uncertainty and disturbances.
The assumption will be that the past data is constant as one is already at steady-state.

## Slide 6: State space predictions
The output prediction equations (one step ahead) must be same as the current steady-state. We need the predictions to be time invariant and this will happened automatically if the signals have all converged to a suitable steady-state.
One can easily ensure a match with the actual process output by defining the disturbance estimate as follows:
HENCE the correct disturbance estimate is critical to ensure unbiased predictions.

## Slide 7: Example
Viewers might like to prove to themselves that given the conditions provided, the following output predictions are indeed constant and correct (=yp).

## Slide 8: Generic use of a disturbance estimate
One can predict the future using just the model steady-state gain, if the system is in steady-state and hence:
Hence the output predictions will be unbiased if we can ensure that:
In other words, can we find a good value for the disturbance estimate?

## Slide 9: Generic use of a disturbance estimate
A suitable disturbance estimate is easy to find. By definition one can write that the current output is measured and therefore:
Substitute this into the relevant equation and thus:
Obviously both Gm(0) and u are known!

## Slide 10: Remark
Often for convenience the model output is considered to have no inherent disturbance and hence:
In this case, the ‘disturbance’ signal to correct the output predictions for unknown disturbances and parameter errors can be determined using:
Measured process output
Model output

## Slide 11: What happens if not in steady-state?
In practice the system is rarely in steady-state so one needs to formulate an estimate of the disturbance for such cases to ensure the predictions are still unbiased.
It transpires that the simple formulae derived last is the most convenient and appropriate – also we know this works exactly in the steady-state!
Strictly the ‘disturbance’ estimate is capturing the effect of parameter uncertainty as well as real disturbances.

## Slide 12: Independent model formulation
A common way of forming predictions is to run a simple model in parallel with the actual process.
Gp
yp
Gm
ym
u
d
dm
process
Model Gm is used both to form nominal predictions and the bias term dm.

## Slide 13: Summary of unbiased predictions
A common tool to ensure unbiased predictions is the use of a disturbance estimate.
This term captures both the actual system disturbance and caters for any errors in the parameters.
The use of this prediction model will ensure exactly correct prediction at steady-state and thus the model will not cause any steady-state bias in the control action.

## Slide 14
© 2014 University of Sheffield
This work is licensed under the Creative Commons Attribution 2.0 UK: England & Wales Licence. To view a copy of this licence, visit http://creativecommons.org/licenses/by/2.0/uk/ or send a letter to: Creative Commons, 171 Second Street, Suite 300, San Francisco, California 94105, USA.
It should be noted that some of the materials contained within this resource are subject to third party rights and any copyright notices must remain with these materials in the event of reuse or repurposing.
If there are third party images within the resource please do not remove or alter any of the copyright notices or website details shown below the image.
(Please list details of the third party rights contained within this work.
If you include your institutions logo on the cover please include reference to the fact that it is a trade mark and all copyright in that image is reserved.)
Anthony Rossiter
Department of Automatic Control and Systems Engineering
University of Sheffield
www.shef.ac.uk/acse