## Slide 1: Predictive control 13 Measuring performance
Anthony Rossiter

## Slide 2: Introduction
We have established that using prediction and/or anticipation within control is logical and shown how predictions can be formulated from a number of common discrete models.
The main components of an MPC law were summarised as: Prediction, Receding horizon, Modelling, Performance index, Degrees of freedom, Constraint handling, Multivariable.
This video looks at the performance index.

## Slide 3: Performance index
When undertaking control design, the designer must have in their mind some requirements which can be used to compare alternatives.
How do we know if control law 1 is better than control law 2? The answer is usually because it meets the requirements better in some sense.
Which response is best and why?

## Slide 4: Performance index
Often humans use rather vague performance indices when making choices and we trade of between different aspects such as rise-time, overshoot and settling time in somewhat arbitrary ways.
MPC is typically based on a precise numerical optimum, consequently a much more precise definition of ‘optimum’ performance is required.
However, this definition can be viewed as being equally arbitrary and is simply a tool to enable a unique solution.

## Slide 5: Examples of different performance indices
Fastest settling time (to within say 5%).
Smallest actuation energy (to avoid fatigue and minimise fuel costs).
Smallest error on average.
Fastest rise time (so operating close to target).
Minimise the maximum deviation when subject to a disturbance (ensures quality remains within given tolerance).
etc
The problem with many of these criteria is that they are non-linear in parameters we can choose and thus do not lead to tractable optimisations.

## Slide 6: Reminder
A conventional feedback loop gives nonlinear and non-simple dependencies such as:

## Slide 7: Examples of different performance indices
Fastest settling time.
What is the link between settling time and the parameters of a control law – not analytic in general?
Smallest actuation energy
How is actuation energy computed and how does this depend on the parameters of a control law?
Smallest error
This is equivalent to something like:
The problem with many of these criteria is that they are non-linear in parameters we can choose and thus do not lead to tractable optimisations.

## Slide 8: Tractable performance index
In order for a performance index to lead to simple optimisations, the terms it includes should:
Have linear (or simple) dependence on any parameters we can choose.
Be a continuous function, and with continuous derivatives. [Non-continuity makes any optimisation much more challenging.]

## Slide 9: Simple measures of performance
Functions which have continuous derivatives.
Functions which have a unique minimum.
Functions which do not contain non-linearities (e.g. |a| requires knowledge of when a<0).
Functions which are always positive – negative cost is meaningless and could be misleading.
Polynomials and exponential broadly meet the above. Sinusoids do not have a unique minimum and exponentials have no stationary points.
F=ax+b can go to –∞ and thus is meaningless.
Cubics and higher order have multiple stationary points.
Quadratics only remain.

## Slide 10: Simple measures of performance
Performance based on quadratics lead to sensible engineering and simple optimisations.
In engineering, energy terms often link to the square of a state, thus assessing x2 is logical.
x2 terms are always positive for any ‘x’.
A quadratic penalises larger deviations heavily, but not small ones, which often makes good sense.
Critically, the optimum changes smoothly and slowly with small changes in parameters and thus behaviour is not erratic.

## Slide 11: Summary
The use of quadratic performance indices is the most common choice within the literature and tends to result in smooth and robust control designs.
Some early work looked at 1-norms and ∞–norms, for example in the parametric case and the robust case (handling uncertainty) so the optimisation is complex anyway. However the lack of much focus in this area is unsurprising.
Ironically perhaps, this means that MPC typically adopts performance indices similar or identical to LQR strategies.

## Slide 12
© 2014 University of Sheffield
This work is licensed under the Creative Commons Attribution 2.0 UK: England & Wales Licence. To view a copy of this licence, visit http://creativecommons.org/licenses/by/2.0/uk/ or send a letter to: Creative Commons, 171 Second Street, Suite 300, San Francisco, California 94105, USA.
It should be noted that some of the materials contained within this resource are subject to third party rights and any copyright notices must remain with these materials in the event of reuse or repurposing.
If there are third party images within the resource please do not remove or alter any of the copyright notices or website details shown below the image.
(Please list details of the third party rights contained within this work.
If you include your institutions logo on the cover please include reference to the fact that it is a trade mark and all copyright in that image is reserved.)
Anthony Rossiter
Department of Automatic Control and Systems Engineering
University of Sheffield
www.shef.ac.uk/acse