## Slide 1: Predictive control 14 Typical MPC performance index
Anthony Rossiter

## Slide 2: Introduction
We have established that a performance index comprising quadratic terms is likely to lead to easier optimisations and smoother outcomes.
This video introduces typical performance indices based on quadratic terms and shows how these relate to common sense.

## Slide 3: Output predictions and errors
Indicate the errors between the predicted output and the target at a number of specified sampling instants.
Predicted future
Past

## Slide 4: Performance index
It is reasonable to say that performance is linked to the predicted (or expected) output errors.
The smaller J, the better the expected tracking performance.
NOTE: One needs to determine an appropriate ‘n’; this is discussed later.

## Slide 5: Simple J inappropriate
However a simple J such as this will not lead to sensible control decisions in general.
Consider the system G:
Choose a future input sequence to minimise J!
The danger is that one can find an input sequence which makes all the errors =0 by inverting the plant!

## Slide 6: Simple J inappropriate
A simple J such as this will not lead to sensible control decisions in general. Zero errors give:
Clearly a divergent signal.
Cannot use a cost based just on tracking errors in general.

## Slide 7: Simple J inappropriate
A simple J such as this will not lead to sensible control decisions in general. A more typical realisation (based on GPC) gives plots like this.
Input signal is very large.
Output converges very quickly as expected - errors are small!

## Slide 8: Performance index
While performance is linked to the predicted (or expected) output errors, it is also clear that for practical systems, users are also concerned about actuation.
Too much actuation causes fatigue, or is simply expensive in fuel, or requires over specification of valves, etc.
Consequently, it is logical also to penalise the input signal.

## Slide 9: Performance index still wrong
While this performance index seems to include what you want, tracking errors and input activity, it is in fact ill-posed as a steady-state analysis will show.
In general, cannot converge to correct target.
Cannot drive both the error and the input to zero simultaneously!

## Slide 10: Summary
The use of quadratic performance indices is the most common choice within the literature and tends to result in smooth and robust control designs.
However, one cannot naively choose some function of the square of tracking errors alone as this will not result in the desired control actions.
Similarly, one cannot just add in the square of input actions to reduce control activity, as this will result in steady-state offset, that is the performance index is ill-posed.
The next video introduces performance indices that work.

## Slide 11
© 2014 University of Sheffield
This work is licensed under the Creative Commons Attribution 2.0 UK: England & Wales Licence. To view a copy of this licence, visit http://creativecommons.org/licenses/by/2.0/uk/ or send a letter to: Creative Commons, 171 Second Street, Suite 300, San Francisco, California 94105, USA.
It should be noted that some of the materials contained within this resource are subject to third party rights and any copyright notices must remain with these materials in the event of reuse or repurposing.
If there are third party images within the resource please do not remove or alter any of the copyright notices or website details shown below the image.
(Please list details of the third party rights contained within this work.
If you include your institutions logo on the cover please include reference to the fact that it is a trade mark and all copyright in that image is reserved.)
Anthony Rossiter
Department of Automatic Control and Systems Engineering
University of Sheffield
www.shef.ac.uk/acse