## Slide 1: Predictive control 15 Unbiased performance index
Anthony Rossiter

## Slide 2: Introduction
We have established that a performance index comprising quadratic terms is likely to lead to easier optimisations and smoother outcomes.
However, we have also seen that a naïve use of quadratic terms need not imply sensible outcomes.
This video introduces the concept of an unbiased performance index needed to ensure that the optimisations are well posed and expected to give sensible answers.

## Slide 3: Performance index background
It has been established that the performance index should penalise tracking errors and input activity.
However, a simplistic realisation does not work.
In general, cannot converge to correct target.
Cannot drive both the error and the input to zero simultaneously!

## Slide 4: Why is this performance index wrong?
It is not possible to simultaneously drive both the tracking error and the input to zero!
Logically one should begin from the ideal finish point which is as follows:
A simple idea would be to penalise the deviations from the desired steady-state as, by definition, driving these deviations to zero will drive the output to the desired value.

## Slide 5: Reminder
An earlier video looked at unbiased predictions and proposed the following for state space models:
First, estimate the steady-state values of disturbance/states/inputs to ensure consistency between the model and process and thus define the deviation variables.
Do predictions about the estimated steady-state using nominal process parameters.

## Slide 6: Summary
The use of unbiased predictions in combination with an unbiased performance index based on quadratic terms is expected to give a sensible outcome.
Specifically, a steady-state analysis will show that, if the closed-loop system converges, it must converge to the correct steady-state.
Convergence, tuning, etc are topics for later videos.

## Slide 7: Alternative performance indices
The key attribute of the performance index is that it is unbiased, and we can think of several other unbiased performance indices.
Unbiased, in simple terms, means that if we deploy the performance index at the correct steady-state, then it will propose that the input remains unchanged.
Most obvious terms are those which are zero at the correct steady-state.
Some common components, and hence a generic choice of J, that satisfy this requirement are listed here.
Assumes constant r

## Slide 8: Alternative performance indices
A generic choice of J, that satisfies the unbiased requirement, can be given as.
It is more typical in the literature to see the following two alternatives.
Assumes constant r
Penalises distance of input from the steady-state.
Penalises the rate of change of the input. This probably has a closer link to fatigue.

## Slide 9: Horizons and weights in J
So far these videos have given the performance index in a very simplified form, using the same horizons for the inputs and outputs and scalar weights. A more generic form is as follows.
Matrix weights on each term.
Different horizons for inputs and outputs. (There is some discussion in the community about the role of these which is covered later.)

## Slide 10: Summary
The use of quadratic performance indices is the most common choice within the literature and tends to result in smooth and robust control designs.
However, one cannot naively choose some function of the square of tracking errors alone as this will not result in the desired control actions.
This video has summarised a typical performance index which ensures the system will converge to the correct steady-state (assuming it converges at all).
Discussion of the choices within this performance index will be covered in the later videos.

## Slide 11: Addendum
There are some in the community who feel the use of a performance index is rather artificial and the choices of weights somewhat arbitrary.
They propose ‘encouraging’ system predictions to follow a given dynamic path, as the desired time constants may be known. This approach can be straightforward for simple SISO systems.
However, it is easy to show that the latter approach is in fact equally arbitrary and does not lend itself to convenient analysis, guarantees of good behaviour, constraint handling or MIMO processes.

## Slide 12
© 2014 University of Sheffield
This work is licensed under the Creative Commons Attribution 2.0 UK: England & Wales Licence. To view a copy of this licence, visit http://creativecommons.org/licenses/by/2.0/uk/ or send a letter to: Creative Commons, 171 Second Street, Suite 300, San Francisco, California 94105, USA.
It should be noted that some of the materials contained within this resource are subject to third party rights and any copyright notices must remain with these materials in the event of reuse or repurposing.
If there are third party images within the resource please do not remove or alter any of the copyright notices or website details shown below the image.
(Please list details of the third party rights contained within this work.
If you include your institutions logo on the cover please include reference to the fact that it is a trade mark and all copyright in that image is reserved.)
Anthony Rossiter
Department of Automatic Control and Systems Engineering
University of Sheffield
www.shef.ac.uk/acse