## Slide 1: Predictive control 2 Main components
Anthony Rossiter

## Slide 2: Introduction
We have established that using prediction and/or anticipation within control is logical – humans do this naturally.
Therefore it makes good sense to consider how such concepts can be embedded into an automated control strategy.
This video introduces the core concepts which underpin the use of prediction before later videos consider those in more detail.

## Slide 3: Main components of MPC
Prediction
Receding horizon
Modelling
Performance index
Degrees of freedom
Constraint handling
Multivariable
The key to effective implementation is a clear understanding of how MPC works!
Readers should not attempt algorithm design and tuning before they have the required understanding or they could make silly mistakes which result in poor implementations.

## Slide 4: Prediction
Some key questions are as follows:
Why is prediction important?
How far should we predict?
Consequences of not predicting.
How do we predict?
How accurate do predictions need to be?
A number of simple analogies will help to explore these and give the viewer an understanding of good answers.
Readers should not attempt algorithm design and tuning before they have the required understanding or they could make silly mistakes which result in poor implementations.

## Slide 5: Why is prediction important?
Any parent will get ‘fed up’ telling their children to think of possible consequences before they act.
Jumped of shed roof – broken ankle.
Used knife incorrectly – badly cut finger.
Spoke back at a teacher – lots of detentions.
Didn’t consult bus timetable before going out – had a long wait at 11pm at night!
Viewers will have many of their own examples.
Before planning an activity, always think through all the likely consequences and possibilities, otherwise the outcome may be far from desirable!

## Slide 6: How far should we predict?
Prediction horizon is an often misunderstood concept in MPC and ‘treated’ as a tuning parameter by many misguided users.
However, in terms of normal human behaviour, we all know how far ahead we should predict and the consequences of getting this wrong.
When driving, what prediction horizon is used and why? What happens when it is foggy?
When heating a house, what prediction horizon is used and why?
When moving a very heavy item, what prediction horizon is used?
One always predicts beyond the safe braking distance, otherwise one cannot give a reasonable guarantee of avoiding a crash.
Prediction horizon > settling time!
One always considers the time at which the house needs to be warm enough, and we turn the heating on sufficiently far in advance – that is beyond the settling time.
Prediction horizon > settling time!
One considers the whole trajectory, lifting, carrying and putting down again. Otherwise one could drop the item at a place which causes serious damage.
Prediction horizon > settling time!

## Slide 7: Summary of prediction horizon
Common sense analysis of everyday scenarios tells us that we must always predict beyond the key dynamics of a process, otherwise the dynamic part we have not observed (and thus excluded in our decision process) could come back and bite us!
If we only predict 20m ahead while doing 70mph, then a sharp corner will inevitably cause a crash.
If we only predict 20min ahead with house heating, the house will not be warm enough in time.
If we only plan 3m ahead while carrying a heavy object, we may not allow for a critical obstacle en-route.

## Slide 8: Receding horizon
This concept may be over complicated in the literature.
All it means is that we continually update our predictions and decision making to take account of the most recent target and measurement data.
The effect is that the prediction horizon is always relative to the current position, and thus recedes away from the viewer as the viewer moves forward
Current position
Predicting to this position
t=0
t=1
t=2
Horizon stays the same!

## Slide 9: Feedback from MPC
Viewers may hear the argument that the receding horizon introduces feedback.
In fact, one could be more careful and say that the continual update of predictions and decision making to take account of the most recent target and measurement data introduces feedback.
Measurement is a core part of a feedback loop.
Decisions based on measurement are the 2nd core part.
Predictive control incorporates both.

## Slide 10: Modelling with MPC
A core part of prediction control is the prediction.
While humans are very good at predicting outcomes, these predictions are based on a lot of experience which could be difficult to untangle and automate.
In order to automate predictions, implicitly we are modelling system behaviour and thus a model is required.
However, what is not immediately obvious is how we go about defining or determining an appropriate prediction model.

## Slide 11: Modelling requirements
Easy to form predictions – ideally linear.
Easy to identify model parameters.
Gives accurate predictions.
Of course these are all somewhat vague.
What do we mean by accurate: steady-state, fast transients, mid-response, … ?
What parameter identification algorithm is being proposed and does this give a model which is most accurate? Most simple black-box methods are based on one-step ahead prediction errors, thus fast transients only!

## Slide 12: Modelling summary
The simplest model that gives accurate enough predictions is usually best.
Accurate enough is ill-defined, but in practice predictions can often be 10-20% out in the steady-state and still be highly effective as long as they also capture the key dynamic changes during transients.
It is rarely beneficial to spend excessive effort improving accuracy as this is expensive, can give high order models but may have little impact on behaviour.
Feedback will correct for small modelling errors.
Make sure you check the ability of your model to give good long range prediction.

## Slide 13: Move to next video

## Slide 14
© 2014 University of Sheffield
This work is licensed under the Creative Commons Attribution 2.0 UK: England & Wales Licence. To view a copy of this licence, visit http://creativecommons.org/licenses/by/2.0/uk/ or send a letter to: Creative Commons, 171 Second Street, Suite 300, San Francisco, California 94105, USA.
It should be noted that some of the materials contained within this resource are subject to third party rights and any copyright notices must remain with these materials in the event of reuse or repurposing.
If there are third party images within the resource please do not remove or alter any of the copyright notices or website details shown below the image.
(Please list details of the third party rights contained within this work.
If you include your institutions logo on the cover please include reference to the fact that it is a trade mark and all copyright in that image is reserved.)
Anthony Rossiter
Department of Automatic Control and Systems Engineering
University of Sheffield
www.shef.ac.uk/acse