## Slide 1: Predictive control 3 Main components continued
Anthony Rossiter

## Slide 2: Continued from previous video

## Slide 3: Performance index
Implicitly humans have an internal measure of what constitutes good and bad behaviour, although this will rarely be quantitative.
SLOW
OSCILLATORY
UNSTABLE
IDEAL
Target settling time

## Slide 4: Performance index
Some typical questions one needs to tackle are as follows:
What is the performance index used for?
How should the performance index be designed?
How can we handle trade offs between optimal and safe/robust performance.
What performance indices do humans use in every day life? How do these change as we get older e.g. (babies to adults)? Is this insight useful?

## Slide 5: What is the performance index used for?
In order to automate a predictive control strategy, that is to decide which input trajectory is best, one needs a precise numeric definition of ‘best’.
The performance index is a numeric definition for best.
REMARK: Viewers make like to note that there is still an inherent contradiction in that the performance index is still to some extent arbitrary as it is rarely possible to link this to real economics.

## Slide 6: How should the performance index be designed?
General guidance suggests that simpler definitions are better as they lead to better conditioned and simpler optimisations.
As the optimisation is carried out online, with corresponding risks, this should only have increased complexity where the benefits are clear.
REMARK: Typically quadratic performance indices are used as these give well conditioned optimisations with a unique minimum and generally smooth behaviours.
1-norm and inf-norm for example often result in non-smooth behaviours and can be highly sensitive.

## Slide 7: Human behaviours
How do human performance indices change as we get older e.g. (babies to adults)?
RACQUET SPORTS
A beginner has a very simple strategy, get the ball back across the net, anywhere and anyhow!
An intermediate is more sophisticated, not only get the ball back, but do so with some measure of control and direction.
An expert has a very complex strategy. Not only get the ball back, but be very precise on how, sometimes planning several shots ahead in order to create an opening.
As we get older and more experienced, our performance indices become more demanding!
Same insight applies to walking, driving, cooking, etc.

## Slide 8: Modelling and performance
The reason our performance indices become more challenging is because our internal model is better (through experience). Hence a simple insight follows:
Little experience or low quality model
Cautious performance index at most is realistic.
Lots of experience or high quality model
Ambitious performance index is possible (but not necessary)

## Slide 9: Human behaviours
How can we handle trade offs between optimal and safe/robust performance?
RACQUET SPORTS
A player uses a very complex strategy. Not only get the ball back, but be very precise on how, that is trying to hit the lines.
A player has a simple strategy of simply keeping the ball in play, for example aiming for the middle.
Who is more likely to make a mistake? [Assume the opponent is passive]
Same insight applies to driving (think of racing), cooking, robotics, etc.

## Slide 10: High performance demand
High performance demands are not cost free:
High performance implies high risk
High risk means less robustness or ability to deal with uncertainty.
Low performance with a high fidelity model (low risk)
If working well within capacity, a strategy is likely to be safe and robust to uncertainty.

## Slide 11: How many degrees of freedom?
Degrees of freedom describes the complexity of the input predictions.
Consequently this issue is closely linked to the previous discussion on performance indices.
There is no point utilising high numbers of degrees of freedom in conjunction with a highly demanding performance index, if the model is poor.
The result of any corresponding optimisation would be largely meaningless, just as it would be to ask a beginner in racquet sports to construct and play an elaborate 5-10 shot rally!
The useful number of d.o.f. is linked to prediction accuracy.

## Slide 12: Ill-posed performance index
Imagine a scenario with a very demanding performance index which requires someone to follow an elaborate trajectory, but now give them only one degree of freedom.
A simple analogy is to model a sine wave with a 1st order polynomial!
Or follow a corner in 50yds by turning the steering wheel now!
This is an example of an ill-posed problem. With just one d.o.f., one can only use a simple performance index and simple target.
Time varying targets need high numbers of d.o.f.

## Slide 13: Ill-posed performance index
Imagine a scenario with a low prediction horizon compared to the system dynamics and use numerous d.o.f. to optimise tracking within that horizon.
A simple analogy is to fit data in a small domain whereas in fact one needs data fitted over a much larger domain.
Optimising the speed of a car looking only 50yds ahead may result in excessive speeds so one cannot take a corner that was just beyond 50yds so unobserved.
This is an example of an ill-posed problem. With low horizons one cannot fully anticipate the full consequences of ones actions, so the planned actions may be very poor.
Advance information can only be used well with high numbers of d.o.f.
51yds
100mph
DATA FIT LOOKS OK in RESTRICTED DOMAIN

## Slide 14: Constraint handling
One major advantage of predictive control is that it embeds constraints into the strategy development.
The proposed input trajectory is optimal while satisfying constraints.
More typical control strategies treat constraints as an after thought.
The systematic embedding of constraint information is critical to getting effective and robust closed-loop behaviour.

## Slide 15: Example of importance of constraints
Form a PI control law with good speed of response, settling time, for a tank level control system. Typical control design guidelines allow for up to a 25% overshoot.
A control scheme for a nuclear reactor assumes that the input can reach 110%. What happens when this saturates at 100%?
The level overshoot is a disaster as chemical spills everywhere!
The input constraint means one loses control and an explosion follows.
In both cases the underlying control laws were good and robust, so long as one did not operate close to constraints.

## Slide 16: How is predictive control different?
The constraints are embedded into the planning.
Predictive control will not propose input flows that allow the tank to overflow. This may result in slightly slower rise times during transients, but it will be safe.
Predictive control will be aware that the input is limited to 100% and thus will not allow earlier input choices which make the system not stabilisable thereafter.
In general, embedding constraints (awareness of kerbs while driving, flow or power limits in process control, speed limits for a robot, etc.) will ensure that the proposed input strategies are optimised, always and the tuning changes if needs be for different operating points.
A simple well tuned but unconstrained law may be very effective in a small range, but disastrous if used over a wider operating range.

## Slide 17: Multivariable/interaction
There are many examples of processes which have numerous inputs and outputs.
A car has 2 main inputs (throttle and steering) and 2 outputs (speed and direction).
A aeroplane has numerous control surfaces and moves in 3D space.
A chemical reaction could be affected by flow rates of reactants, heat supply, pressure and the outputs could be speed of reaction (production rate), quality, purity, etc.
A key observation is that for multivariable processes, often changing one input changes all the outputs and therefore an effective control law has to consider all inputs and outputs simultaneously.

## Slide 18: Handling interaction
Anyone who has learnt to fly a helicopter, or perhaps even cycle, will realise that humans struggle to develop effective strategies for interactive processes.
We can cope up to 2-3 inputs/outputs and beyond that a human is not an ideal controller!
A similar observation applies to classical control techniques such as PID, lead and lag.
One advantage of MPC is that it is framework that automatically takes account of interaction, although of course we need to express the algorithm in mathematical language and get a computer to do the number crunching.

## Slide 19: Summary
We have shown the key concepts underpinning predictive control, these are:
Prediction Receding horizon Modelling Performance index Degrees of freedom Constraint handling Multivariable
A GOOD UNDERSTANDING OF THESE CONCEPTS WILL ENSURE THAT THE VIEWER COMES UP WITH A PREDICTIVE CONTROL ALGORITHM THAT MAKES GOOD SENSE AND THUS IS LIKELY TO BE EFFECTIVE.

## Slide 20: Summary – well posed MPC
Modelling efforts should be focussed on efficacy for prediction, including dependence on d.o.f..
Predictions must capture all the transient and steady-state behaviour.
Prediction class should include the desired closed-loop behaviour (not be too simple/low order).
Performance indices must be realistic and matched to model accuracy.
Constraints must be built in from the beginning.
Efficient computation requires linear models and simple parameterisations of d.o.f.

## Slide 21
© 2014 University of Sheffield
This work is licensed under the Creative Commons Attribution 2.0 UK: England & Wales Licence. To view a copy of this licence, visit http://creativecommons.org/licenses/by/2.0/uk/ or send a letter to: Creative Commons, 171 Second Street, Suite 300, San Francisco, California 94105, USA.
It should be noted that some of the materials contained within this resource are subject to third party rights and any copyright notices must remain with these materials in the event of reuse or repurposing.
If there are third party images within the resource please do not remove or alter any of the copyright notices or website details shown below the image.
(Please list details of the third party rights contained within this work.
If you include your institutions logo on the cover please include reference to the fact that it is a trade mark and all copyright in that image is reserved.)
Anthony Rossiter
Department of Automatic Control and Systems Engineering
University of Sheffield
www.shef.ac.uk/acse