## Slide 1: Predictive control 4 Modelling
Anthony Rossiter

## Slide 2: Introduction
The previous videos introduced the main concepts underpinning predictive control (MPC).
However, these were presented in a simple human centred fashion.
To automate MPC, it is necessary to present these concepts in mathematical terms.
This video begins that process by looking at modelling.
Models are required for prediction and thus logically are tackled first.

## Slide 3: Model requirements
Simple manipulation and algebra requires linear models as then superposition can be used.
MPC deploys linear models whenever these are good enough.
These videos do not discuss non-linear models and the associated MPC – there is huge variety in that topic and it is far beyond taught course level.
Typical linear models are transfer function or state-space. To some extent step response models are a subset of transfer functions.

## Slide 4: Discrete or continuous
While processes operate in continuous time and indeed so do classical control laws such as PI, decision making tends to be more of a discrete process.
Decision making requires processing time and thus cannot be instantaneous, especially where one is considering interacting inputs/outputs/constraints and performance.
Common predictive control laws are implemented in discrete time.
While continuous time variants exist in the literature, the author is not aware of much take up in industry.

## Slide 5: What sample rate?
Several different issues govern the best choice of sample rate.
A typical argument is that one wants around 10 sample points within a typical response (settling time or rise time?).
Slower decision making than this will reduce ability to get high performance or to respond to disturbances fast enough.

## Slide 6: Why not sample very fast?
Let the input change very frequently, here at about 100 times the rise time.
The inherent ‘lag’ (small high freq. gain) within a real system will not respond to these high frequency changes!
Using a high sample rate is pointless:
The system cannot respond to fast input changes.
It increases the number of decision variables, which implies a more challenging optimisation.
INPUT
OUTPUT

## Slide 7: Interim summary
Operate in discrete time.
Use a sample rate around 1/10 of principle system dynamic responses.
The 2nd assumption is somewhat loose so can be modified if disturbance rejection or performance is not good enough.

## Slide 8: State space models
A common discrete state space model is given as:
This video series will restrict itself to this form and assume, for convenience, that D=0.
Viewers who understand the basic concepts will be easily able to rework fine details as required to deal with modifications in this form, more general disturbances and so forth.
State
Output
Disturbance
input

## Slide 9: Transfer function models
The most common transfer function model with MPC is the so called CARIMA model.
This subsumes in its structure many other popular forms.
It is used because the uncertainty is included in a way that is a good representation of slowly varying disturbances that could have a non-zero steady-state.
Zero mean random variable
Rather clumsy so not advised for MIMO processes.

## Slide 10: Step response models
A step response model is a particular form of transfer function model.
Originally popular because the step response is the most readily available characteristic for many process systems.
Has the weakness of requiring a large number of parameters (technically infinite).
Disturbances are estimated as a difference between the model output and measured output.
Disturbance estimate also captures the effect of unknown initial conditions
Input increment

## Slide 11: Independent model
The idea here is that the model G can be anything (state space, transfer function, step response, etc.) and is considered in isolation from real plant measurements.
The actual future ‘predicted’ outputs are taken from the independent model + an offset term to represent the expected constant difference between the model and true process.
Offset estimate captures the effect of differences between model and plant.

## Slide 12: Summary
It is common to use discrete models in predictive control.
These models can take whatever form the user wants, but the algorithm is much easier to code and implement if simple linear models are used.
A typical sample rate will be about 1/10 of the timescale of the principle dynamics. Again this can be modified if necessary, but much faster or slower would normally be nonsensical.

## Slide 13
© 2014 University of Sheffield
This work is licensed under the Creative Commons Attribution 2.0 UK: England & Wales Licence. To view a copy of this licence, visit http://creativecommons.org/licenses/by/2.0/uk/ or send a letter to: Creative Commons, 171 Second Street, Suite 300, San Francisco, California 94105, USA.
It should be noted that some of the materials contained within this resource are subject to third party rights and any copyright notices must remain with these materials in the event of reuse or repurposing.
If there are third party images within the resource please do not remove or alter any of the copyright notices or website details shown below the image.
(Please list details of the third party rights contained within this work.
If you include your institutions logo on the cover please include reference to the fact that it is a trade mark and all copyright in that image is reserved.)
Anthony Rossiter
Department of Automatic Control and Systems Engineering
University of Sheffield
www.shef.ac.uk/acse