## Slide 1: Predictive control 7 prediction with CARIMA models
Anthony Rossiter

## Slide 2: Introduction
The previous videos introduced the main concepts underpinning predictive control (MPC).
They also argued that linear discrete models are a logical basis for any predictions.
This video considers how predictions can be formed from an underlying transfer function model.
The initial focus is on SISO systems as the algebra for MIMO is rather messy with transfer functions and hence not to be recommended.
Dimensions are not stated except where possibly unclear.

## Slide 3: CARIMA model
The most common transfer function model with MPC is the so called CARIMA model.
This subsumes in its structure many other popular forms.
It is used because the uncertainty is included in a way that is a good representation of slowly varying disturbances that could have a non-zero steady-state.
Zero mean random variable
Although T(z) could arise from a model identification, in practice it is treated as a design parameter.

## Slide 4: Basic concepts of prediction
Discrete models are one-step ahead prediction models, that is, given data at sample ‘k’, one can determine data at sample ‘k+1’.
Disturbance estimate
To reduce notation, this video will not use the double subscript notation of yk+i|k as the meaning is clear.

## Slide 5: Significance of CARIMA model
The reason a CARIMA model is used is that it incorporates a disturbance estimate and therefore can give unbiased predictions in the steady-state, irrespective of some parameter uncertainty.
Zero mean random variable
In practice, the incremental form is used for predictions – implicitly this is based on changes rather than absolute values.

## Slide 6: CARIMA model
For convenience, as the output is often measured, the 1-step ahead prediction models uses variables of the output and input increment and assumes that the best estimate of the future ‘random’ term is zero.
Combine a(z) and Delta
Use input increments

## Slide 7: Basic concepts of prediction with a CARIMA model
Discrete models are one-step ahead prediction models, that is, given data at sample ‘k’, one can determine data at sample ‘k+1’.
No need for a disturbance estimate in this prediction model as implicit within the use of increments.

## Slide 8: Basic concept of prediction
The one-step ahead prediction can be used recursively to find an n-step ahead prediction as follows:
Use the 1 step ahead to find yk+1, then substitute this into the next equation to find yk+2, then use yk+1 yk+2 to determine yk+3 and keep iterating through to yk+n .
HOWEVER: This is tedious and better methods do exist.

## Slide 9: Set of prediction equations
The entire set of one-step ahead prediction equations can be considered as set of simultaneous equations where the unknowns are the predicted future outputs.
In the example here there are 4 unknowns and 4 equations. Remember that future inputs are decision variables not unknowns.

## Slide 10: Solving for the output predictions
Simultaneous equations can be represented using matrix/vector format, after which the solution is obvious. An illustration and some suitable notation is given here which clearly separates past and future variables.

## Slide 11: Similarly
Simultaneous equations can be represented using matrix/vector format, after which the solution is obvious. An illustration and some suitable notation is given here which clearly separates past and future variables.
NOTE: For convenience a single unit delay in b(z) is ignored in forming these matrices and assumed in the corresponding algebra.

## Slide 12: Combining the previous 2 slides gives
Use the shorthand notation to give a compact description of the entire predictions.
Next, re-introduce the arrow notation deployed in the previous video, and hence:

## Slide 13: Solving for output predictions
Now the prediction variables are in compact matrix/vector format, one can easily re-arrange to find the dependence of the output predictions upon past (or known) data and the decision variables.
Decision variables (future input increments)
Known or past data

## Slide 14: Summary
It is common to use discrete models for prediction.
This video has shown how CARIMA models can be used to form n-step ahead predictions.
It is also shown how predictions can be separated into known parts (based on measurements or past data) and unknown parts (based on decision variables yet to be selected).
The predictions are grouped in vector format for convenience of handling hereafter.
While this video did not consider MIMO transfer functions, identical conceptual steps can be used.

## Slide 15
© 2014 University of Sheffield
This work is licensed under the Creative Commons Attribution 2.0 UK: England & Wales Licence. To view a copy of this licence, visit http://creativecommons.org/licenses/by/2.0/uk/ or send a letter to: Creative Commons, 171 Second Street, Suite 300, San Francisco, California 94105, USA.
It should be noted that some of the materials contained within this resource are subject to third party rights and any copyright notices must remain with these materials in the event of reuse or repurposing.
If there are third party images within the resource please do not remove or alter any of the copyright notices or website details shown below the image.
(Please list details of the third party rights contained within this work.
If you include your institutions logo on the cover please include reference to the fact that it is a trade mark and all copyright in that image is reserved.)
Anthony Rossiter
Department of Automatic Control and Systems Engineering
University of Sheffield
www.shef.ac.uk/acse