## Slide 1: CHAPTER 2 Generalised Predictive Control 1 Introduction
Anthony Rossiter

## Slide 2: What is Generalised Predictive Control (GPC)?
GPC was first proposed by Clarke and co-workers in the 1980s.
It draws together lots of the existing the thinking and algorithms on predictive control at the time into a single algorithm.
Conceptually equivalent to Dynamic Matrix Control (DMC) which is very popular in industry.
GPC/DMC have many theoretical weaknesses, but for most cases avoiding these is straightforward and hence widely adopted and successful.

## Slide 3: This chapter
Main aim is to develop the core components within a GPC (DMC) algorithm and show how these are use to derive a control law.
Later chapters look at analysis, tuning and how to avoid poor performance.
Indications are given of problems/scenarios where GPC/DMC should be avoided.
Consideration is given to loop sensitivity, but in an introductory manner only.
MATLAB code for implementing GPC is provided for simple model types.
Discussion of constraints is left to a later chapter.

## Slide 4: Base line assumptions
The first set of videos in the MPC series set out the foundations of a typical algorithm.
The use of unbiased predictions (open-loop for now), for example:
The use of an unbiased cost.
This set of videos looks at the combination of these two components and analyses the resulting control law.

## Slide 5: Notation
Viewers are reminded of the arrow notation for capturing predictions, that is vectors of vectors.
Right arrow implies prediction.
Left arrow implies past data.
Horizons must be defined elsewhere as not explicit in the notation.

## Slide 6: Outstanding issues
What are the degrees of freedom within the predictions?
How does one put the predictions into the performance index in an algebraically neat and transparent fashion which makes the role of the degrees of freedom obvious.
This video looks at these two issues.

## Slide 7: Degrees of freedom
The predictions in the previous chapter were constructed assuming all the future inputs could be selected.
In practice such a numeric computation would be intractable (unless a simple algebraic solution existed).
Consequently, it is necessary to select a subset of the future inputs and assume the other values are known.
In practice, this is done by assuming the input (within the predictions) becomes fixed after nu steps.

## Slide 8: Typical future inputs
If one is using CARIMA model and the associated predictions, then
nu values can be selected to change the predictions
After nu steps, the input increments are assumed to be zero.

## Slide 9: Illustration of prediction structure
Input increments
Inputs
nu samples

## Slide 10: Typical future inputs
If one is using a state space model and deviation variables:
nu values can be selected to change the predictions
After nu steps, the input assumed to be at some steady-state (must be fixed to 0 for no offset).

## Slide 11: Illustration of prediction structure
Input deviations
Inputs
nu samples
uss
us

## Slide 12: Simplifying the performance index
The basic performance index includes summation terms which are rather messy to handle when one needs to do optimisation and the like.
However, there is a simple trick to turn a sum of squares into a single term which is easy to handle. Lets do the SISO case first.

## Slide 13: MIMO system performance index
If each error term is a vector in itself, as would be the case for a MIMO system, a similar trick suffices.
Same formulae as for SISO case!

## Slide 14: Key components summary
This video has summarised the key components for a GPC law in a compact fashion.
Assume the input changes only over the 1st nu steps which implies a specific structure for the vectors:
Rewrite the performance index in terms of vectors to remove the summing notation and thus give a simple convenient expression, e.g.:

## Slide 15
© 2014 University of Sheffield
This work is licensed under the Creative Commons Attribution 2.0 UK: England & Wales Licence. To view a copy of this licence, visit http://creativecommons.org/licenses/by/2.0/uk/ or send a letter to: Creative Commons, 171 Second Street, Suite 300, San Francisco, California 94105, USA.
It should be noted that some of the materials contained within this resource are subject to third party rights and any copyright notices must remain with these materials in the event of reuse or repurposing.
If there are third party images within the resource please do not remove or alter any of the copyright notices or website details shown below the image.
(Please list details of the third party rights contained within this work.
If you include your institutions logo on the cover please include reference to the fact that it is a trade mark and all copyright in that image is reserved.)
Anthony Rossiter
Department of Automatic Control and Systems Engineering
University of Sheffield
www.shef.ac.uk/acse