## Slide 1: CHAPTER 2 Generalised Predictive Control 2 The performance index
Anthony Rossiter

## Slide 2: Introduction
The previous video outlined the basic components of a GPC control law, that is the prediction structure and the performance index.
Specifically it was noted that one forces the input predictions to a fixed value after nu steps which puts a particular structure into the vectors of future inputs. These vectors comprise the d.o.f. in any optimisation.
The sum of squares of tracking errors and control errors was expressed in a compact form using vectors of predictions.

## Slide 3: This video
We have defined the predictions.
We have a clear handle on the d.o.f. within the predictions (1st nu values of the input).
We have defined the performance index.
We have expressed the performance index neatly in terms of the predictions.
Consequently we can put the predictions and the performance index together and perform a minimisation to find the ‘optimum’ value of the d.o.f.

## Slide 4: GPC – CARIMA model
The predictions are given as:
The performance index (assuming simple weights) is given as:

## Slide 5: Remark on H
The predictions include a square matrix H.
However, given we know the structure of the future inputs is:
H1 is tall and thin.
In practice, for convenience, authors just write H (not H1) and assume this is defined to have the relevant number of columns (equivalent to nu samples).
An equivalent statement holds for deviation variables.

## Slide 6: Substitute predictions into J
Substituting predictions into J gives the following:

## Slide 7: Simplifying the performance index
Substituting predictions into J gives the following:

## Slide 8: Optimising functions of many variables
As the performance index is quadratic and strictly positive we know it has a unique minimum.
We also know that this minimum is characterised by the gradient being zero.
For a function of many variables, the gradient is defined as follows:

## Slide 9: Gradient of simple vector functions
It is useful to check the gradient of simple functions of a vector, two examples are given next:

## Slide 10: Gradient of simple vector functions
It is useful to check the gradient of simple quadratic functions of a vector. Here we use result of the previous slide and the product rule for differentiation:

## Slide 11: Combining observations
Let us draw together everything we know so far:
Required optimisation
Gradient of functions of a vector
We need to find the gradient of J with respect to the vector of future input increments

## Slide 12: Combining observations
Let us draw together everything we know so far:
The optimum trajectory of future control increments depends linearly on the future target and past inputs/outputs.

## Slide 13: Practical implementation
The first set of videos discussed the fact that the optimisation is carried out at every sampling instant, that is one continually revisits earlier decisions.
Hence, even though the optimisation sets out a viable long term plan of future control increments, only the first of these is implemented as one wants to improve any other choices.
The control law is defined then from the 1st value of the optimum input trajectory.

## Slide 14: Extracting the 1st value
Assume that the vector of future input increments is organised by sample, then the 1st block can be extracted as follows.
GPC control law!

## Slide 15: Summary of GPC
A GPC control law is determined by minimising the performance index wrt to the first nu future control increments, assuming increments beyond this are zero.
As the performance index is quadratic, it has a unique minimum that can be obtained using a gradient operator, that is gradient is zero.
The control law is given by the first value of the future control trajectory, as this is the control increment to be implemented now (proposed future control increments will be adjusted and improved at later samples).
The control law is linear in measured values and the target.

## Slide 16
© 2014 University of Sheffield
This work is licensed under the Creative Commons Attribution 2.0 UK: England & Wales Licence. To view a copy of this licence, visit http://creativecommons.org/licenses/by/2.0/uk/ or send a letter to: Creative Commons, 171 Second Street, Suite 300, San Francisco, California 94105, USA.
It should be noted that some of the materials contained within this resource are subject to third party rights and any copyright notices must remain with these materials in the event of reuse or repurposing.
If there are third party images within the resource please do not remove or alter any of the copyright notices or website details shown below the image.
(Please list details of the third party rights contained within this work.
If you include your institutions logo on the cover please include reference to the fact that it is a trade mark and all copyright in that image is reserved.)
Anthony Rossiter
Department of Automatic Control and Systems Engineering
University of Sheffield
www.shef.ac.uk/acse