## Slide 1: CHAPTER 2 Generalised Predictive Control 9 Numerical examples with a T-filter
Anthony Rossiter

## Slide 2: Introduction
The previous videos demonstrated how a T-filter modifies prediction and hence a GPC control law.
This video will demonstrate the impact on a number of examples.
  MATLAB code for finding predictions.
  MATLAB code for the control law.
  Simulation comparisons with and without a T-filter.
  Sensitivity functions.

## Slide 3: Example 1
Take a system G(z) with nu=3, ny=8 and lambda=1.
[H,P,Q] = mpc_predmat(a,b,ny)
[Pt,Qt] = mpc_predtfilt(H,P,Q,Tfilt,sizey,ny);
[Nk,Dk,Pr,] = mpc_law(H,P,Q,nu,lambda,1,sizey)
[Nkt,Dkt] = mpc_law(H,Pt,Qt,nu,lambda,1,sizey)
Pc = mpc_poles(a,b,Nk,Dk)
Pct = mpc_poles_tfilter(a,b,Nkt,Dkt,Tfilt)
Go to MATLAB to demonstrate.
video2_9_example1.m

## Slide 4: Example 2
Take a system G(z) with nu=6, ny=15 and lambda=3.
Go to MATLAB to demonstrate.
video2_9_example2.m

## Slide 5: Tracking performance
The next file shows a simulation with a set point change but not disturbances and no noise.
It is clear that the responses with and without the T-filter are identical, even though the controller parameters are different.
Go to MATLAB to demonstrate.
video2_9_example3.m

## Slide 6: Disturbance rejection
The next file shows a simulation with a set point change followed by a step disturbance but no noise.
It is clear that the responses with and without the T-filter are very different and indeed, if anything, using a T-filter has made the disturbance rejection worse (SLOWER TO RESPOND)!
video2_9_example4.m
Edit the file to try examples of your own.

## Slide 7: Noise rejection
The next file shows a simulation with no set point change and no disturbance but includes noise.
It is clear that the responses with and without the T-filter are very different. The T-filter has made the input responses much less active.
video2_9_example5.m
Try changing the choice of T-filter for all these examples and see what the impact is.

## Slide 8: Sensitivity functions
We can plot the frequency response for the sensitivity functions and get a view of how sensitivity is affected for low and high frequency uncertainty.
Here we focus on the impact on the input signal (actuation).
video2_9_example6.m

## Slide 9: Summary
A T-filter changes loop sensitivity and control law parameters but NOT nominal behaviour and poles.
The actual impact is difficult to discern in advance but typical expectations are:
  Stronger filtering reduces input variance for high frequency noise.
  Stronger filtering can make disturbance rejection slower.
Experience shows usually a T-filter helps but proposals in the literature for systematic design are weak at best!
A possible suggestion is to match the dominant open-loop poles.

## Slide 10: REMARKS
For convenience and transparency, the examples in this video are all SISO.
The same concepts and insights will carry over to the MIMO case, but coding and plotting would be more cumbersome.
The requirement for a T-filter is closed allied to the use of a CARIMA model which is best suited to the SISO case anyway, thus alternatives are likely to be better for the MIMO case.

## Slide 11
© 2014 University of Sheffield
This work is licensed under the Creative Commons Attribution 2.0 UK: England & Wales Licence. To view a copy of this licence, visit http://creativecommons.org/licenses/by/2.0/uk/ or send a letter to: Creative Commons, 171 Second Street, Suite 300, San Francisco, California 94105, USA.
It should be noted that some of the materials contained within this resource are subject to third party rights and any copyright notices must remain with these materials in the event of reuse or repurposing.
If there are third party images within the resource please do not remove or alter any of the copyright notices or website details shown below the image.
(Please list details of the third party rights contained within this work.
If you include your institutions logo on the cover please include reference to the fact that it is a trade mark and all copyright in that image is reserved.)
Anthony Rossiter
Department of Automatic Control and Systems Engineering
University of Sheffield
www.shef.ac.uk/acse