## Slide 1: CHAPTER 5 Predictive Control with constraints 11 simple implementation for dual-mode approaches with tracking
Anthony Rossiter

## Slide 2: Background
The previous two videos demonstrated how one could incorporate constraints into an OMPC/SOMPC algorithm.
In simple terms, the easiest method is to form an autonomous model formulation for the predictions and express constraints at each sample using some inequalities.
Finally, use the admissible set algorithm to define the constraints over an infinite prediction horizon in terms of a finite set of inequalities linked to the d.o.f.
However, the simple extension to tracking scenarios was inflexible and not suitable for online implementation.
This video considers an alternative procedure for forming MCAS which incorporates a time varying target and disturbance.
The approach is simple, but also has obvious weaknesses.

## Slide 3: Background continued
The difficulty with doing constraint handling of a dual-mode approach is that predictions evolve over an infinite horizon.
Consequently, one can only be sure that the ‘optimal’ solution is valid (feasible), if it satisfies constraints over an infinite horizon.
The previous videos used admissible sets to capture the required inequalities.
However, admissible sets are defined for a fixed scenario and thus do not allow time varying components such as the steady-state.
Here f changes every sample.

## Slide 4: A pragmatic approach
We know that in practice, for given scenarios, the admissible set algorithm converges after a finite number of iterations.
The number of iterations is linked to the closed-loop poles, and the proximity of the steady-state to a constraint.
For typical closed-loop poles around 0.8-0.9, this iteration count will be 10-20, but would only reach numbers like 40 for ‘unusual cases’ (very slow poles, etc.).
We could simple define the constraints for the first 30-40 samples, accepting this has large degree of redundancy, and assume that this captures the MCAS fully (which it will for most normal cases).

## Slide 5: Predicting in absolute values
It is convenient to construct the predictions in terms of absolute values.

## Slide 6: Predicting in absolute values
Prediction was covered in chapters 1, so details omitted here. Using the model below, predictions are easy to compute for a desired horizon.

## Slide 7: Constraint inequalities
These can be constructed in an exactly analogous manner to video5_3 of this chapter.
For example, combine the following:
The re-organisation is omitted here as obvious.

## Slide 8: Summary of constraint inequalities
Constraints on inputs and states, for a specified prediction horizon, can be combined into a single set of inequalities within which the target and disturbance signal appear explicitly.
In a more conventional set arrangement.
Notation used in sompc_constraints.m code

## Slide 9: Pragmatic versus admissible set
Admissible set
Unique and efficient.
Easy to remove redundant constraints offline.
Only defined for fixed (r-d).
If (r-d) changes, the set must be recomputed on-line ; this is non-trivial.
Pragmatic
Requires ‘arbitrary’ choice of horizon.
Cannot easily identify and remove redundant constraints.
Allows any value of (r-d) and captures the MCAS for any reasonable choices.
Does not need to be updated online as (r-d) changes because the dependence is embedded.
Code more flexible.
Where efficiency is not important, for example messing about in your office, the pragmatic choice is probably easier.

## Slide 10: Numerical examples
In the ompcold subfolder of OMPC folder.
video5_11_example1.m, video5_11_example2.m, video5_11_example3.m
These files demonstrate that the set point and disturbance can be modified online without any change to the inequalities for constraint handling.
The downside is the rather large number of constraints (many redundant) and potentially conservative choice of predictive horizon.
Avoids the need to predefine limits on or values for the target and disturbance which are needed to use admissible sets.

## Slide 11: REMARK
It is not obvious which inequalities may be redundant because these inequalities put no limits on (r-d).
For example, it would be easy to propose a value for (r-d) for which the MCAS is empty!
Or, a value for r-d which required an excessively long prediction horizon to capture the MCAS (e.g. steady-state on boundary).

## Slide 12: Summary
This video has given an alternative to admissible sets for constraint handling over an infinite horizon.
The assumption is made that using the insight from admissible sets, we know that constraints do not need to be tested explicitly beyond some horizon ‘n’, but this ‘n’ will vary with the scenario (set point, disturbance, etc.).
Nevertheless, ensuring predictions meet constraints for some arbitrary large ‘n’ is likely to capture the MCAS and thus allow simple coding.
Specifically, the set does not need re-computing each time the set point/disturbance changes.
The focus here is on being pragmatic, not rigorous, as often that is enough for testing concepts and learning.

## Slide 13
© 2014 University of Sheffield
This work is licensed under the Creative Commons Attribution 2.0 UK: England & Wales Licence. To view a copy of this licence, visit http://creativecommons.org/licenses/by/2.0/uk/ or send a letter to: Creative Commons, 171 Second Street, Suite 300, San Francisco, California 94105, USA.
It should be noted that some of the materials contained within this resource are subject to third party rights and any copyright notices must remain with these materials in the event of reuse or repurposing.
If there are third party images within the resource please do not remove or alter any of the copyright notices or website details shown below the image.
(Please list details of the third party rights contained within this work.
If you include your institutions logo on the cover please include reference to the fact that it is a trade mark and all copyright in that image is reserved.)
Anthony Rossiter
Department of Automatic Control and Systems Engineering
University of Sheffield
www.shef.ac.uk/acse