## Slide 1: CHAPTER 5 Predictive Control with constraints 12 reachable targets for dual-mode approaches with tracking
Anthony Rossiter

## Slide 2: Background
The previous three videos demonstrated how one could incorporate constraints into an OMPC/SOMPC algorithm.
  One method is to form an autonomous model formulation for the predictions and express constraints at each sample using some inequalities.
  Then use the admissible set algorithm to define the constraints over an infinite prediction horizon in terms of a finite set of inequalities linked to the d.o.f.
However, the simple extension to tracking scenarios was inflexible and not suitable for online implementation.
  An alternative pragmatic approach extended easily to tracking scenarios but potentially required excessive numbers of inequalities and did not have a simple formal guarantee of capturing the MCAS.
This video considers the general implications of allowing targets and disturbances to change in conjunction with a dual-mode prediction and demonstrates this implies hard limits on allowable values.

## Slide 3: Maximal admissible set
Express predictions in the form:
Express constraints at each sample in the form:
A critical requirement to ensure convergence is that the asymptotic point is strictly inside the MCAS, not on the boundary.

## Slide 4: Tracking with SOMPC/OMPC
Earlier it was proposed to write the performance index and predictions in terms of the deviation variables:
Can we make these meet the MAS requirements while allowing r, d to change?
NOW we modify the proposal slightly:
Use deviation variables in J; hence the cost depends only on c!.
Use absolute values in the constraint handling and integrate the term (r-d) as an additional state in the autonomous prediction model.

## Slide 5: Control Law in absolute values
Substituting in for the estimated steady-state gives.
In essence the autonomous prediction model has extra states in (r-d)!
Because the prediction model has a state (r-d), this will appear as a state in any admissible set algorithm and therefore must meet the same criteria as other states (boundedness, convergence, etc.).
If (r-d) is not constrained, the other states cannot be constrained to the requirement to converge strictly inside the set!

## Slide 6: Typical constraints
Using absolute values.
Augmented state

## Slide 7: Combined constraints
Using this augmented state in the constraint equations gives:
A key issue is the definition of limits on r and d.

## Slide 8: Constraints on targets/disturbances
We cannot choose any target or assume any magnitude disturbance. The notional state and input constraints can be satisfied iff the target is sensible.
The steady-state must lie in the interior of the constraints set (for inputs and states).

## Slide 9: Requirements on constraints
The steady-state must lie in the interior of the set.
Postulate a given target/disturbance pair, then the steady-state is given as:
Key requirements are that:

## Slide 10: Requirements on constraints
The steady-state must lie in the interior of the set.

## Slide 11: Requirements on constraints
The steady-state must lie in the interior of the set.
Users should check their targets against these inequalities before deploying.
WARNING: This is necessary but not sufficient for the target to be feasible.

## Slide 12: video5_12_example1.m
Demonstrates the feasible region for limits on r-d given certain limits on the input and states.
In practice the upper limit must exceed the lower limit.

## Slide 13: Summary
This video has shown that in order for a well defined constrained problem to exist, the target must be reachable.
One can define necessary (not sufficient) conditions for reachability, e.g.:
In general, beyond remit of this video, one may need tighter limits to ensure a target is feasible.
Viewers may note that subtleties such as these are usually omitted from journal papers or avoided by using constant targets such as the origin.

## Slide 14
© 2014 University of Sheffield
This work is licensed under the Creative Commons Attribution 2.0 UK: England & Wales Licence. To view a copy of this licence, visit http://creativecommons.org/licenses/by/2.0/uk/ or send a letter to: Creative Commons, 171 Second Street, Suite 300, San Francisco, California 94105, USA.
It should be noted that some of the materials contained within this resource are subject to third party rights and any copyright notices must remain with these materials in the event of reuse or repurposing.
If there are third party images within the resource please do not remove or alter any of the copyright notices or website details shown below the image.
(Please list details of the third party rights contained within this work.
If you include your institutions logo on the cover please include reference to the fact that it is a trade mark and all copyright in that image is reserved.)
Anthony Rossiter
Department of Automatic Control and Systems Engineering
University of Sheffield
www.shef.ac.uk/acse