## Slide 1: CHAPTER 3 Well posed predictive control 4 Changing the input horizons
Anthony Rossiter

## Slide 2: Introduction
The previous videos demonstrated, through examples and simple argument, that the use of an input horizon of 1, for most cases, resulted in a poorly defined optimisation.
With low output horizons, the optimisation does not reflect enough of the predicted behaviour to be meaningful.
With high output horizons, the steady-state error dominates J and thus the control move goes directly to the steady-state.
For systems with undesirable open-loop dynamics, there is insufficient flexibility with the predicted control trajectory to form desirable predictions.
The main exception was where open-loop dynamics were acceptable.
Unsurprisingly then, this video looks at increasing the control horizon.

## Slide 3: Alternatives
This video focuses mainly on investigating the impact of choosing nu=2,3,4,…
HOWEVER there still remains the possibility of having a low and high output horizon.
  It is important to confirm whether the same insights as determined with nu=1 apply when nu is larger.
  There is also some subtlety in what constitutes a large enough, but not too large, output horizon.
The reader is reminded that SISO examples are used as these illustrate the key concepts clearly.
The same principles will carry across to the MIMO case.

## Slide 4: Aside - feedforward
So far these videos are assuming there is no advance information on the target, so in essence the feedforward Pr is a constant and the target is assumed constant.
Discussions on how ‘tuning’ guidance might change when advance information on the target is available is delayed until later so as not to confuse core concepts.
However, viewers should note that there is a very strong link between nu and behaviour when feedforward is provided.

## Slide 5: Begin with some examples using nu=2

## Slide 6: gpc3_4_example1, nu=2
Low ny, predictions are poor.
Higher ny, predictions improve.
Notable that for high ny
steady-state error is small and this means in effect one has only a single d.o.f., the first control move.

## Slide 7: gpc3_4_example1, nu=2
If control weighting is increased, a higher ny is needed to capture the whole prediction and thus for J to be well posed.
The dominance of the
steady-state error depends upon both weighting and horizon – the analytical link will be non simple.

## Slide 8: Open-loop prediction vs closed-loop
The actual closed-loop behaviour may be similar to the open-loop within the horizon, but is this similar enough to say the optimisation is well-posed?
For nu=2 the optimisation may be well-posed for lower ny, but predictions and closed-loop only overlap in some cases and may do so better or worse with high ny.

## Slide 9: gpc3_4_example2.m with nu=2
NMP, so a low ny does not work in general.
As horizon increases, predictions improve.
Here we need ny close to 40 before the optimisation is well–posed.

## Slide 10: Open-loop prediction vs closed-loop
The actual closed-loop behaviour may be similar to the open-loop within the horizon, but is this similar enough to say the optimisation is well-posed?
For nu=2 the closed-loop is still different from the predictions, even with larger ny.
However, the differences are small enough to explain why GPC often works!

## Slide 11: gpc3_4_example3.m with nu=2
Simple real poles, but one unstable.
Better predictions than with nu=1, but still divergent!!
Increasing ny helps up to a point, but make ny too large and numerical ill-conditionning dominates!
Remember H,P,Q made up of divergent predictions.

## Slide 12: gpc3_4_example 4 with nu=2
Complex poles, but stable.
Overall prediction strategy is quite poor.
Increasing ny has little impact here because nu=2 is still too small to overcome unpleasant open-loop dynamics.

## Slide 13: Observation summary for nu=2
Long output horizons reduce the steady-state error in the predictions and hence ensure that the performance index J is more representative of real behaviour and could be considered well-posed.
With low output horizons, it is clear that the part of the prediction with J is not representative of the whole behaviour, and thus the optimisation is not well-posed.
HOWEVER: while increasing ny seems to help in general:
  This does not follow for open-loop unstable processes.
  Low input horizons still cause fundamental problems where a system has difficult open-loop dynamics.
A choice of nu=2 seems to give better predictions than nu=1. Consequently, one may struggle to justify the use of nu=1 where a well-posed optimisation is desired.

## Slide 14
© 2014 University of Sheffield
This work is licensed under the Creative Commons Attribution 2.0 UK: England & Wales Licence. To view a copy of this licence, visit http://creativecommons.org/licenses/by/2.0/uk/ or send a letter to: Creative Commons, 171 Second Street, Suite 300, San Francisco, California 94105, USA.
It should be noted that some of the materials contained within this resource are subject to third party rights and any copyright notices must remain with these materials in the event of reuse or repurposing.
If there are third party images within the resource please do not remove or alter any of the copyright notices or website details shown below the image.
(Please list details of the third party rights contained within this work.
If you include your institutions logo on the cover please include reference to the fact that it is a trade mark and all copyright in that image is reserved.)
Anthony Rossiter
Department of Automatic Control and Systems Engineering
University of Sheffield
www.shef.ac.uk/acse