## Slide 1: CHAPTER 3 Well posed predictive control 6 Changing the input weighting
Anthony Rossiter

## Slide 2: Introduction
The previous videos demonstrated, through examples and simple argument, that a large output horizon and an input horizon of at least 3, but possible greater, are needed to ensure that the optimum predictions are sensible and thus allow a well posed optimisation.
So far however, the examples have not considered the impact of the weighting matrices upon the optimisation.
For MIMO systems, the selection of good weights to appropriately value behaviour in different loops could be quite an art and I am sceptical that one could be particularly systematic without some form of real economic function.
However, for SISO systems, one can reduce the performance index to having a single weight, and this does allow some insight and thus pseudo-systematic design.
This video overlays plots with several different weights simultaneously in an effort to gain insight into the interaction between the weight and the horizons.

## Slide 3: Typical performance index
Assuming GPC for now (similar insights will follow for other performance indices), J was given as:
In the SISO case there is a single weight to express the relative importance of actuator movement as compared to tracking errors.
The principle is that larger λ implies smaller control increments (less actuator fatigue) but consequently the tracking errors would be larger.
However, are there other impacts?

## Slide 4: Choice of parameters
For simplicity, this video will often use fixed values of ny=15, nu=4 as these values seem to be ‘large enough’ based on the earlier videos.
We will then explore the impact of changing λ.
However, as will be seen, what constitutes a long enough prediction horizon and large enough control horizon is not fixed!

## Slide 5: Aside - feedforward
So far these videos are assuming there is no advance information on the target, so in essence the feedforward Pr is a constant and the target is assumed constant.
Discussions on how ‘tuning’ guidance might change when advance information on the target is available is delayed until later so as not to confuse core concepts.
However, viewers should note that there is a very strong link between nu and behaviour when feedforward is provided.

## Slide 6: gpc3_6_example1
For small λ, the predictions beyond the horizon are good, so the optimisation is well posed.
For large λ, the predictions not included in J (that is beyond ny) are poor, and this indicates that optimising J does not imply good overall predictions.

## Slide 7: gpc3_6_example1
One might think that simply increasing the output horizon would be good enough, but clearly the predictions still have a sizeable offset in steady-state.
This is because the inputs are forced to a constant after nu samples!
High input weighting implies small increments in the control and therefore we need far more than 4 control moves to get to steady state. nu must be larger!
We need to take nu up to 15 before the predictions have no obvious offset!

## Slide 8: gpc3_6_example2
For this example, the predictions are not good for any choice of λ, but for different reasons.
The system has a slow mode, so ny=15 is too small to capture all the open-loop dynamics.
If λ is large, this issue is exaggerated even more due to slow input moves.

## Slide 9: gpc3_6_example2
Try a larger ny.
The predictions are better, but still the offset is poor.
Again, the issue here is likely to be the restriction to just 4 control moves to both optimise predicted performance, and reach steady-state.
With nu=10, the lower weighted algorithms do well.
The highest weighting needs nu close to 20!

## Slide 10: gpc3_6_example3
For an unstable system, large values for λ can be problematic.
A high gain controller is needed, and so slowing down the control increments is counter productive.
This is clearly seen in the plots where behaviour gets worse as the weighting increases.
Changes to nu and ny are not likely to change much of the insight here as there are other issues with open-loop unstable processes.

## Slide 11: gpc3_6_example4
Once again it is noted that for large values of λ the default horizons of ny=15, nu=4 are just not large enough.
The horizons must be large enough to capture the expected performance, with the magnitude of input increments that is allowed.
In this case we needed to take nu up to 25 to get satisfactory predictions.
It is clear that the inputs are changing over the whole horizon.

## Slide 12: Reflections
To get a well posed optimisation, both the input and output horizon have to be large enough.
The output horizon must include enough of the steady-state errors so that the long term predictions match what is really wanted.
The obvious test is that the predictions do indeed go close to the steady-state.
The input horizon must include enough terms so that the control increments can:
get the system to correct steady-state.
counter any undesirable dynamics in the open-loop.
Have sufficient flexibility remaining to optimise transient performance.

## Slide 13: Reflections on horizons
Long enough cannot easily be defined in advance.
The output horizon must be many samples longer than it takes the predictions to get to steady-state.
This tends to mean well over the open-loop settling time, especially if the control action is smooth (not aggressive).
The input horizon should be long enough to capture the ‘ideal’ closed-loop input trajectory.
This could be close to the open-loop settling time but is dependent upon the target tuning (FAST or SLOW).
In practise, for many cases a smaller nu gives a similar first choice of u(k) – but is this accident rather than design?

## Slide 14: CONCLUSIONS
The horizons ny and nu are not tuning parameters or indeed ‘options’.
If not chosen correctly and systematically, then the optimisation will be ill-posed in that optimising J need not imply sensible or good overall trajectories.
Optimising J, tells you the best with restricted d.o.f. over a restricted horizon and this could be seriously flawed.
You can have confidence with GPC/DMC if and only if the horizons are long enough – it may take some offline testing to be sure of this.
The required horizons may change with the control weighting. Start from your expected ideal closed-loop responses!

## Slide 15: CAVIAT
Viewers may note many examples where GPC appears to give poorly defined predictions, and yet the closed-loop implementation gives reasonable behaviour.
In essence the use of feedback, updating every sample, can sometimes save an otherwise ill-thought through strategy.
My view however is that, these examples work more by accident than design and therefore you should exercise extreme caution.
Why do it poorly when you can do it well?

## Slide 16
© 2014 University of Sheffield
This work is licensed under the Creative Commons Attribution 2.0 UK: England & Wales Licence. To view a copy of this licence, visit http://creativecommons.org/licenses/by/2.0/uk/ or send a letter to: Creative Commons, 171 Second Street, Suite 300, San Francisco, California 94105, USA.
It should be noted that some of the materials contained within this resource are subject to third party rights and any copyright notices must remain with these materials in the event of reuse or repurposing.
If there are third party images within the resource please do not remove or alter any of the copyright notices or website details shown below the image.
(Please list details of the third party rights contained within this work.
If you include your institutions logo on the cover please include reference to the fact that it is a trade mark and all copyright in that image is reserved.)
Anthony Rossiter
Department of Automatic Control and Systems Engineering
University of Sheffield
www.shef.ac.uk/acse